## Slide 1
I²C Communication Protocol
National Telecommunication Institute (NTI)
Digital IC Design Using FPGA — RTL Implementation and Verification
Team members :
Ahmed Shaaban Elnegaar
Hazim Osama shams elden
Mohamed Abdel Sadek

## Slide 2
1. Introduction
I²C provides a simple synchronous serial interface using two shared lines: SDA and SCL.
The design contains an I²C Master, I²C Slave, clock-divider function, shared open-drain bus, FSM controllers, and verification testbench.
The system supports both write and read transactions.
The project verifies operation using a self-checking testbench.

## Slide 3
2. Project Objectives
Design a complete functional I²C communication system in Verilog HDL.
Implement both Master and Slave modules.
Support Master → Slave write transactions and Slave → Master read transactions.
Verify communication scenarios using a self-checking testbench.
Provide monitoring and debugging signals for internal operation.

## Slide 4
3. I²C Protocol Fundamentals
I²C = Inter-Integrated Circuit protocol.
A synchronous serial communication protocol using a shared two-wire bus.
SCL: Serial Clock Line generated by the Master in this implementation.
SDA: Bidirectional Serial Data Line shared by all devices.
Target implementation clock: 100 kHz SCL.

## Slide 5
4. Open-Drain Bus Operation
Master
Slave
Pull-Up Resistor
Devices can drive SDA LOW or release it to high impedance (Z).
No device actively drives SDA HIGH.
When all devices release SDA, the external pull-up resistor makes the bus HIGH.
The same principle is used for SCL in the implementation's bus interface.

## Slide 6
5. Transmission Rules
• Data is transferred in 8-bit bytes.
• Bits are sampled while SCL is HIGH; SDA only changes when SCL is LOW.
• Standard transfer rates: 100 kbps (Standard mode) and 400 kbps (Fast mode).

## Slide 7
6. START, STOP and ACK/NACK
Start condition (S): SDA goes LOW while SCL is HIGH. This wakes the slaves.
Stop condition (P): SDA goes HIGH while SCL is HIGH. This signals the end of communication.

## Slide 8
7. Communication Sequence

## Slide 9
8. System Architecture
Clock Divider 50 MHz → 100 kHz
I²C Master
Shared SDA / SCL Bus
I²C Slave
Top level contains Master controller, Slave controller, clock-divider function, and shared SDA/SCL bus.
The Master initiates transactions and controls SCL.
The Slave monitors the bus and responds only when its address is detected.

## Slide 10
System Architecrture

## Slide 11
9. Master FSM

## Slide 12
10. Slave FSM

## Slide 15
Schematic_master

## Slide 16
Schematic_master

## Slide 17
Schematic_slave

## Slide 19
Waveform

## Slide 22
Results
Simulation confirmed:
• The master correctly initiates start/stop conditions.
• The slave acknowledges when addressed.
• Data transfers successfully between master and slave.
• ACK/NACK behavior matches specification.
• Debug signals help visualize FSM progression.

## Slide 23
Thank You
Questions?